## Slide 1
CLIENT-SIDE BIOPHOTONICS
Pulse from Pixels — Toss the Sensor
Camera-Based Photoplethysmography (PPG) Vital Signs Monitor
Goal: Measure human heart rate accurately using only a smartphone camera and flashlight LED.
Zero Wearables: Eliminates smartwatches, finger clips, and expensive pulse oximeter hardware.
100% Private in Browser: Video frames stay in transient memory and are discarded immediately. Zero cloud upload.
Modern Tech Stack: Built with React 19, TypeScript, and causal hand-crafted DSP algorithms.
Camera-Based PPG Vital Signs Monitor • Krishnajith KS • ECE Academic Defense

## Slide 2
STAGE 01 / PRINCIPLE OF OPERATION
How Can a Camera See Your Heartbeat?
Photoplethysmography (PPG) & The Beer-Lambert Law
Arterial Pulsation: Every heartbeat pumps blood into the microvascular capillary bed of your fingertip.
Light Absorption: Hemoglobin in blood strongly absorbs green light (~540 nm wavelength).
Microscopic Brightness Shifts: More blood in fingertip = darker frame. Less blood between beats = brighter frame.
Optical Sensing: Phone camera records at 30 frames/second. Spatial averaging converts video frames into a 1D optical pulse wave.
Camera-Based PPG Vital Signs Monitor • Krishnajith KS • ECE Academic Defense

## Slide 3
STAGE 02 / MATHEMATICAL PIPELINE
Step-by-Step Processing Pipeline
From Raw Camera Pixels to Verified Heart Rate
1. Spatial Downsampling: Scales video to 64x64 ROI, extracting spatial mean to save battery and guarantee O(1) memory.
2. Uniform Resampling: Linear interpolation maps jittered mobile timestamps onto an exact 30.0 Hz time grid.
3. 4th-Order Butterworth Filter: Direct Form II SOS removes DC baseline drift, breathing sway, and high-frequency noise.
4. Dual Consensus Engine: Time-domain peak detector cross-checks frequency-domain FFT peak within 3.0 BPM tolerance.
Camera-Based PPG Vital Signs Monitor • Krishnajith KS • ECE Academic Defense

## Slide 4
STAGE 03 / NOISE REJECTION
Cleaning the Signal: Band-Pass Filter
Why We Need a 4th-Order Butterworth Filter
The Noise Problem: Respiration creates slow 0.2 Hz baseline drift. Hand tremor and sensor noise add 10+ Hz spikes.
Passband Window: 0.5 Hz to 4.0 Hz (corresponds to physiological range of 30 BPM to 240 BPM).
Cascaded Biquad Sections: Two 2nd-order Direct Form II Transposed sections give steep 24 dB/octave rolloff.
Maximally Flat: Zero passband ripple prevents false systolic peak distortion.
Camera-Based PPG Vital Signs Monitor • Krishnajith KS • ECE Academic Defense

## Slide 5
STAGE 04 / DUAL ESTIMATION
Dual-Engine Consensus Cross-Check
Preventing False Readings via Time & Frequency Agreement
Method A (Time Domain): Inter-Beat Interval (IBI). Detects systolic wave peaks and calculates BPM = 60 / Delta_t.
Method B (Frequency Domain): 4,096-point Hann-windowed FFT. Finds the dominant spectral power peak frequency f_peak.
Consensus Rule: If |BPM_Time - BPM_Freq| <= 3.0 BPM -> Status: Verified Clean.
Robustness: If hands shake, the two methods disagree (>3.0 BPM) and the system automatically prompts user to steady finger.
Camera-Based PPG Vital Signs Monitor • Krishnajith KS • ECE Academic Defense

## Slide 6
STAGE 05 / ARCHITECTURE & PRIVACY
System Architecture & Memory Discipline
Why Client-Side Matters for Medical Signal Privacy
Zero Server Backend: Entire DSP chain runs locally in browser JavaScript thread and Web Worker. No backend server required.
Strict O(1) Memory Rule: Raw video frames are discarded immediately after computing spatial mean. Zero memory leaks.
Complete Data Privacy: No personal video, camera feed, or physiological data is ever transmitted over network.
Universal Accessibility: Runs on any standard mobile phone or laptop browser via lightweight static web deployment.
Camera-Based PPG Vital Signs Monitor • Krishnajith KS • ECE Academic Defense

## Slide 7
STAGE 06 / USER EXPERIENCE
Landing Page & Presenter Easter Egg
Crumple Editorial Design + Secret Academic Inspection Lab
Public Landing Page: Monochromatic Crumple editorial aesthetic with arterial red pulse disc and AHA resting categories.
Direct Action: "Start Camera" launches capture and transitions smoothly into the monitoring workspace.
Secret Presenter Trigger: Clicking "Developed by Krishnajith KS" 6 times unlocks the Teacher Evaluation Workbench.
Inspection Tools: Multi-channel optical viewport, live waveform stack, viva diagnostics, and synthetic benchmarks (54, 72, 108 BPM).
Camera-Based PPG Vital Signs Monitor • Krishnajith KS • ECE Academic Defense

## Slide 8
STAGE 07 / VIVA DEFENSE CHEAT SHEET
Examiner Questions & Quick Answers
Core ECE Viva Concepts in Plain Language
Q: Why green channel over red? A: Oxygenated hemoglobin absorbs green light (~540nm) 2.5x more strongly, giving superior SNR.
Q: What if phone drops frames? A: Linear resampler maps irregular timestamps to an exact 30 Hz uniform grid so filter cutoffs do not drift.
Q: Why use Direct Form II Biquads? A: Transposed Direct Form II minimizes floating-point roundoff error and state register overhead (flat O(1)).
Q: Is this a clinical medical device? A: No, it is an educational biophotonic DSP monitor demonstrating optical plethysmography in browser.
Camera-Based PPG Vital Signs Monitor • Krishnajith KS • ECE Academic Defense